## Slide 1: MIA Pipeline – Registration
Luca Sahli, Jacob Rasmussen and Camilo Mendez MIA-Lab
Fall 2017

## Slide 2: Overview
Introduction
Evaluation
Affine Registration
BSpline Registration
Discussion
Outlook
Notes: First registration approach
The way we optimzed our registration

## Slide 3: MIA Pipeline
T1_mni
T1_native
Notes: You are all familiar with the MIA Pipepline. We did our work here in the registration, where we registered a T1…
One Example for this registration could be when a patient takes imagaes on different dates or locations and we have
To register the images to each other.

## Slide 4: MIA Pipeline
Evaluation
Notes: You are all familiar with the MIA Pipepline. We did our work here in the registration, where we registered a T1…
One Example for this registration could be when a patient takes imagaes on different dates or locations and we have
To register the images to each other.

## Slide 5: Evaluation
T1_mni
T1_native
Registration
Transformation
Evaluation
T
labels_native
Labels_registerd
labels_registerd
labels_mniatlas
Dice
Notes: Now, how do we get the trasnformarion?
This question is answered by jacob.

## Slide 6: Affine
Affine

## Slide 7: Affine Registration
number_of_histogram_bins: [100, 200, 1000]
learning_rate: [0.1, 0.2, 0.9] step_size: [0.001, 0.01, 0.1] number_of_iterations: [100, 200, 1000] shrink_factors: [(2, 1, 1), (4, 2, 1), (8, 4, 1)] smoothing_sigmas: [(2, 1, 1), (4, 2, 1), (8, 4, 1)]
We use the affine registration class from the MIA Pipeline
Default parameters from SimpleITK
Notes: Uese method from SimpleITK
There are alot of parameters in to set, we tried to opzimize the following:
Metric: Mutual Information
Optimizer: RegularStepGradientDescent
Multi resolution setup
Time: higher more sampling = longer duration

## Slide 8: Optimization
FOR EACH Setting of parameters
FOR 10 patients
Dice[White, Grey, Ventricles] = evaluate()
SAVE mean Dice over the 10 patients
CHOOSE setting with highest Dice
Pseudocode for optimization
Notes: - Number of histogram bins
- Learning rate
- Step size
- Number of iteration
- Shrinking factor
- Smoothing sigma

## Slide 9: Result 1
Dice coefficients affine transformation
Notes: Approximatly tested 930 parameter combinations. 14 sec pro patient
Mean
Ventricles big ranges

## Slide 10: BSpline
BSpline

## Slide 11: BSpline
Definition of a good Registration does not change from affine to Bspline
Optimizer changed from affine to BSpline
Metric changed from affine to BSpline

## Slide 12: Result 2
Affine/ BSpline transformation

## Slide 13: Discussion - Affine
Notes: Ventricles very different.
Volume factor
0.6 still low
Affine limited

## Slide 14: Discussion - BSpline
Notes: -

## Slide 15: Discussion - BSpline
Dice:
White matter 0.51
Grey matter 0.42
Ventricles 0.33
Dice:
White matter 0.62
Grey matter 0.48
Ventricles 0.64
Dice:
White matter 0.64
Grey matter 0.31
Ventricles 0.51
Notes: Ventricles very different.
Volume factor
0.6 still low
Affine limited

## Slide 16: Outlook
SimpleElastix

## Slide 17: Conclusions
SimpleItk is a powerful toolkit
  contains lots of implemented functions for registration
Limited results for affine transformations
BSpline transformation seem to be very promising
  Locally better results (ventricles, bulks in skull)
  However, there are difficulties in choosing right parameters.

## Slide 18: BSpline Registration
number_of_bins: int = 50,
number_of_iterations: int = 1500,
gradient_Convergence_Tolerance: float = 1e-5,
max_number_of_corrections: int = 100,
max_number_of_function_evaluations: int = 1000,
cost_function_convergence_factor: float = 1e+7,
sampling_percentage: float = 0.2,
transformDomainMeshSize = [10,10,10]):
...
We use methods from the SimpleITK library

## Slide 19: Introduction: Registration Pipeline
1. registration
T1_native
T1_mni
labels_
native
labels_
registerd
2. transformation
labels_
mniatlas
3. evaluation
Labels_
registerd
TAffine
TAffine
Dice

## Slide 20: Introduction - sequence
Registration
TAffine
T1_native
T1_mni
labels_native
TAffine
labels_registerd
labels_registerd

## Slide 21: Introduction - evaluation
Dice coefficients
labels_registerd
labels_mniatlas/
ground truth
Evaluator

## Slide 22: Methods
histList = [10, 50, 100, 200, 300]
learnRateList = [0.1, 0.2, 0.9]
iterList = [100, 200, 1000]
Patient 1
..
..
..
mean
Patient 2
..
..
..
Patient 3
..
..
..
Patient 10
..
..
..
…
..
..
..
..
..
..

## Slide 23: Result 2
Dice:
White matter 0.51
Grey matter 0.42
Ventricles 0.33
Mean 0.42
Dice:
White matter 0.62
Grey matter 0.48
Ventricles 0.64
Mean 0.58
Dice:
White matter 0.64
Grey matter 0.31
Ventricles 0.51
Mean 0.49
Begin
Affine
BSpline